## Slide 1: Aerostructures Design of Mechanically Fastened Joints
By
Dr. Mahdi Damghani
2022-2023

## Slide 2: Suggested Readings
Reference 1
Chapter 11 of Ref [1] and Chapter 9 of Ref [2]
Reference 2
By
Niu

## Slide 3: Topics
Familiarisation with joining structures
Familiarisation with mechanically fastened joints
Familiarisation with sizing of bolted joints
Familiarisation with some design rules of bolted joints

## Slide 4: Structural joints
Joints are the most common source of failure in airframes
The affect is not only on static strength but to great extent on fatigue life

## Slide 5: Joints
Mechanically fastened joints (scope of this lecture)
Bonded joints (beyond scope of this lecture)
Hybrid of the above two (beyond scope of this lecture)

## Slide 6: Advantages of mechanically fastened joints
Low production cost
Utilization of conventional metal-working tools and techniques,
Possibility of the riveting process automation,
Ease of inspection
Possibility of their repeated assembling and disassembling for the fabrication replacement or repair
Good hole filling properties of the rivets
A long-standing experience of the industry with riveted joints

## Slide 7: Disadvantages of mechanically fastened joints
A fatigue critical element in metallic airframe construction;
  The rivet installation process imparts elevated stress in the vicinity of the holes.
  The rivet installation process imparts residual stresses in the vicinity of the holes.
frictional forces between the mating sheets induced due to the clamp-up which contribute to fretting damage at the faying surface.

## Slide 8: Failure modes of mechanically fastened joints
Tension failure
Tension cleavage failure
Shear-out failure
Bearing failure
Fastener shear-off
Fastener pull-through

## Slide 9: Common types of joint configurations (Single lap shear joint)
F
F
F
P = F
Interface load
t
d

## Slide 10: Common types of joint configurations (Double lap shear joint)
F
0.5F
P = 0.5F
0.5F
F
P = 0.5F
Interface load

## Slide 11: Common types of joint configurations (Butt joint)
F
F
F
P = F
Interface load

## Slide 12: Common types of joint configurations (L or T joint-1 bolt scenario)
F
F
P = F * Cpr
Prying effect
Prying force can be obtained by conservatively approximating a triangular load distribution and taking moment about the axis of the bolt (see next slide for illustration).

## Slide 13: Illustration of prying force calculation
This approach is conservative and approximate.
13
F
P
Ppr
e
Ppr-eq
2/3*(e-0.5d)
c

## Slide 14: Common types of joint configurations (L or T joint-more than 1 bolt scenario)
F
F
P1 = F * Cpr
Prying effect
P2 = 0
Assuming P2 = 0 is a conservative assumption.

## Slide 15: Common types of joint configurations (L or T joint-more than 1 bolt scenario)
F
P1 = F * Cpr
Prying effect
P2 = 0
e
c
d
t
Some companies use the following Cpr which is very close to the approximate value given in the previous two slides:

## Slide 16
Some General Design Rules

## Slide 17: Design rules 1
d
Edge distance e
Spacing s
Countersunk
holes
t
h
For fatigue critical locations:
For other locations:
For especial circumstances:
Countersunk connections are used for flushed aerodynamic surfaces.
Pan head bolts
Notes: Edge distances larger than two times the hole diameter are recommended, because small edge distances tend to reduce the bearing yielding and ultimately stress (Niu,1989; MMPDS, 2012) and decrease the fatigue life (Niu, 1999).
Besides static failure because of limit loads, the most critical problem observed in metallic joints is failure because of fatigue. When the joint is subjected to cyclic loading during long periods, small cracks may nucleate from hole edges and propagate on the way to the adjacent holes. When compared to static failure, damage because of fatigue presents a larger variability and is influenced by other aspects like hole finishing, interference and plate surface treatments.

## Slide 18: Design rules 2
No threads in bearing (Good practice)
Threads in bearing (Avoid)

## Slide 19
Structural Integrity Assessment Consideration

## Slide 20: Structural integrity assessment 1
The joint must pass all failure modes mentioned in previous slides (Let’s see this in an example).
It is of paramount importance that the efficiency of the joint will be equal to or greater than that of the parent structure.
One side of the joint should not be designed for maximum efficiency at the expense of weight and fabrication cost penalty on the other.
The joint should be located at support structures such as stringers, stiffeners, bulkheads, etc to improve joint efficiency (see next slides for some real examples).
We use average stresses as opposed to real stress distribution for integrity checks (see next slides for illustration).

## Slide 21: Structural integrity assessment 2

## Slide 22: Structural integrity assessment 3
F
F
F
Shear-out planes
Net-tension plane
Bearing plane

## Slide 23: Some terminologies and load path for integrity assessment of joints
The load that passes across the members, usually named the bypass load.
The load that is effectively transferred from one member to the other through the fasteners, that is known as the bearing load.
F
F
Fastener load:
Fastener bearing
stress:
0.35F
0.35F/dt
0.35F
0.35F/dt
0.3F
0.3F/dt
0.65F
0.35F
Bypass load
0.35F
0.65F
Bypass load
0
F
Bypass load
F
0
Bypass load

## Slide 24: Fastener flexibility for integrity assessment of joints
F
F
Fastener load:
0.5F
0.5F
0
Infinitely stiff fasteners:
Infinitely flexible fasteners:
F
F
Fastener load:
0.33F
0.33F
0.33F
F
F
Fastener load:
0.35F
0.35F
0.3F
Actual fasteners:
Notes: The load distribution between the fasteners in the joint has a large impact on factors that affect the strength and fatigue life of the joint, such as bearing pressure and stress concentrations, and is therefore of interest when designing and sizing such a structure.
Fastener flexibility is a property of interest when calculating the load distribution in a joint. It is a measure of the fastener's influence on the flexibility of the joint, and has a large impact on load distribution

## Slide 25: Calculation of fastener flexibility
Available methods are
  Douglas
  Boeing
  Grumman
  Huth (Airbus preferred method)
  Tate and Rosenfeld …

## Slide 26: Calculation of fastener flexibility-Huth
Flexibility = 1/stiffness or mathematically C = 1/K
F
F
E1
E2
Ef
E1:Young’s modulus of plate 1, t1: Thickness of plate 1
E2:Young’s modulus of plate 2, t2: Thickness of plate 2
Ef is Young’s modulus of fastener, d: Fastener shank diameter
Fastener deformation:
Bearing deformation:
Single shear joint n=1
Double shear joint n=2
Bolted metallic joint a=2/3, b=3.0
Riveted metallic joint a=2/5, b=2.2
Bolted composite joint a=2/3, b=4.2

## Slide 27: Calculation of fastener axial stiffness
Notes: N: nut
C: collar

## Slide 28
Finite Element Idealisation

## Slide 29: Idealisation on FEM
1 point model:
Advantage: Reduced time of modelling.
Disadvantage: Model is simplified with the possibility of stress concentration influence due to FEM singularity.
Spring element (CBUSH) with axial and shear stiffness calculated as of previous slides
4/8 point model:
Advantage: Better stress distribution around the diameter, which represents the fastener.
Disadvantage: Meshing is more complicated (depending on the bolt diameter) and time
consuming (TCPU).
Hole model:
Advantage: Better contact representation, different results for tension and compression loading expected.
Disadvantage: Higher level of modelling is required which results to increased calculation
time. In addition, the magnitude of the extracted loads may be affect by the SCF around the hole. This leads to ‘double counting’ the hole influence, since in the filled hole module the SCF is also considered.
Rigid connections (RBE2)

## Slide 30: Example 1
Determine the load capacity of the single lap shear joint of next slide. Assume that sections are thin so effects of load eccentricity can be ignored. The plates are 1.5 mm thick and 25 mm wide made of aluminium 2024-T3. The diameter of fastener is 4 mm. the shear off strength of fastener is 3620 N (2024-T31).
2024-T3 tensile strength = 483 MPa
2024-T3 yield strength = 345 MPa
2024-T3 shear strength = 283 MPa
2024-T3 yield bearing strength = 524 MPa
2024-T3 ultimate bearing strength = 855 MPa
2024-T3 Poisson’s ratio = 0.33
2024-T3 Young’s modulus of elasticity = 73.1 GPa
2024-T3 shear modulus of elasticity = 28 GPa

## Slide 31: Example 1
1.5 mm
1.5 mm
10 mm
F
F
F
F
25 mm

## Slide 32: Solution of example 1
Tension failure:
F
F
25 mm
We are using yield strength as opposed to ultimate strength. This is because after yield, plasticity takes place (particularly at the edge of the hole) then load re-distribution occurs. This is beyond the scope of the lecture.

## Slide 33: Solution of example 1
Tension cleavage failure:
F
F
w = 25
e = 10
0.5(w-d)
P1
P2
P1 is the force in tension section and P2 is the shear force in the shear-out section.

## Slide 34: Solution of example 1
Shear out failure:
F
F
25 mm
e = 10 mm

## Slide 35: Solution of tutorial 1
Bearing failure:
We are using yield bearing strength (limit load of an aircraft). This is because after yield, plasticity takes place and this is local to the hole. Often when this leads to small loads, we do improve the load by accounting for plasticity. This will help design structures that are not prohibitively heavy. So, for aircraft ultimate load then we will use 855MPa as the ultimate bearing stress not 524MPa of yield bearing stress.

## Slide 36: Important note for bearing stress at joints
It is desirable to have joints critical at bearing than shear to achieve the following mechanism particularly at extremely high and short flight manoeuvres loading conditions.
F
F
Limit load
Fastener load
As the external force F increases, extreme bolts will yield and stay at a maximum force called ultimate bearing allowable (purple points). Then the loads of extreme bolts redistribute to internal bolts and they pick up more load. When all the bolts reach maximum force (purple line) the joint fails.
Ultimate load
maximum ultimate bearing allowable

## Slide 37: Solution of example 1
Fastener shear-off failure:
1.5 mm
F
P

## Slide 38: Solution of example 1
Since we assumed load eccentricity is negligible, the fastener works only in shear and this check is not required.
The joint capacity will be the minimum of all forces of failure modes calculated, i.e. 3.144 kN associated to bearing analysis.

## Slide 39: Solution of example 1
Pull-through failure:
F
P
D
t
P’
Depending on the company (Boeing, Aribus, Bombardier, Piaggio, etc), this formula may have some coefficients associated to them such as environmental effects, statistical knockdown factors. However, the core formulation is as above. It is clear that pull-through takes place if there is axial load in the bolt. This scenario is most predominant in T or L joints. For single lap, double lap and butt joints, the pull through can be ignored. For such joints (to take into account effect of load eccentricity) the best practice is the use of Finite Element Analysis to obtain axial and shear forces in the bolts. Then the joint integrity assessment is performed via excel spreadsheet using hand calculation as above. This is the common practice in aerospace industry.
At bolt in rigid metallic fitting in T config and CFRP with symmetric loading:
At bolt in rigid metallic fitting in L config:

## Slide 40
Secondary Bending Moment
(beyond the scope and for information only)

## Slide 41: Effects of secondary bending moment and load eccentricity
This is beyond the scope of the lecture.
The subsequent slides show a simplified approach based on Euler-Bernoulli beam theory which requires solving the governing differential equations of the joint.

## Slide 42: Load eccentricity and secondary bending moment
Maximum total nominal stresses that occur at A and B:
The nominal stresses due to the secondary bending can equal or even exceed the applied stresses. Fractographic investigations of riveted joints indicate that fatigue crack nucleation occurs at the sites of maximum bending stresses.
Notes: See “MODELLING THE SECONDARY BENDING IN RIVETED JOINTS WITH ECCENTRICITIES” by MAŁGORZATA SKORUPA & ADAM KORBEL

## Slide 43: Load eccentricity and secondary bending moment
Simplified approach: In order to derive the bending moment at any site of a joint with eccentricities, the out of plane deformations of the sheets must be known (Euler-Bernoulli). Concepts which enable to compute these deformations, represented by deflections of the joint neutral axis.
The sheets are assumed to act as a single integral beam, the flexural rigidity of which corresponds to the combined thickness of the sheets.
Neutral axis of segment 1
Neutral axis of segment 2
Neutral axis of segment 3
Plane stress
Plane strain
Notes: See “MODELLING THE SECONDARY BENDING IN RIVETED JOINTS WITH ECCENTRICITIES” by MAŁGORZATA SKORUPA & ADAM KORBEL

## Slide 44: Load eccentricity and secondary bending moment
In the case of hinge clamping:
Notes: See “MODELLING THE SECONDARY BENDING IN RIVETED JOINTS WITH ECCENTRICITIES” by MAŁGORZATA SKORUPA & ADAM KORBEL

## Slide 45: Modelling the eccentricities for the lap joint (a) hinged and (b) rigid clamping of the sheet ends
In the case of hinged clampings of the sheet ends, the fixing moments M1A and Mn, B and the reaction V equal zero.

## Slide 46: Why for single lap & double lap shear joints in aerospace applications, the secondary bending moments may be often ignored?
Effect of the applied stress level (S), sheet thickness (t) and the rivet row pitch (p) on the bending factor (kb) and the bending stresses (Sb) at the critical rivet rows for the lap joint
At service loads, due to combination of both high membrane stresses (S) and thin sections, kb tends to hover around unity.
Note that Kb and Sb are nonlinear functions of load (S).
Kb is more sever at lower applied stress (S).
Increasing rivet spacing reduces secondary bending.

## Slide 47
Tutorial Questions & Their Solutions

## Slide 48: Tutorial 1
Determine the load capacity of the single lap shear joint of next slide. Assume that sections are thin so effects of load eccentricity can be ignored. The plates have different thickness and 25 mm wide made of aluminium 2024-T3. The diameter of fastener is 4 mm. the shear off strength of fastener is 3620 N (2024-T31).
2024-T3 tensile strength = 483 MPa
2024-T3 yield strength = 345 MPa
2024-T3 shear strength = 283 MPa
2024-T3 yield bearing strength = 524 MPa
2024-T3 ultimate bearing strength = 855 MPa
2024-T3 Poisson’s ratio = 0.33
2024-T3 Young’s modulus of elasticity = 73.1 GPa
2024-T3 shear modulus of elasticity = 28 GPa

## Slide 49: Tutorial 1
1.5 mm
10 mm
F
F
F
F
25 mm
1 mm

## Slide 50: Solution of tutorial 1
Tension failure:
F
F
25 mm

## Slide 51: Solution of tutorial 1
Tension cleavage failure:
F
F
w = 25
e = 10
0.5(w-d)
P1
P2
P1 is the force in tension section and P2 is the shear force in the shear-out section.

## Slide 52: Solution of tutorial 1
Shear out failure:
F
F
25 mm
e = 10 mm

## Slide 53: Solution of tutorial 1
Bearing failure:

## Slide 54: Solution of tutorial 1
Fastener shear-off failure:
1.5 mm
F
P
1.0 mm
F
P

## Slide 55: Tutorial 2
As a design engineer, propose methods and approaches to reduce joint secondary moments.

## Slide 56: Solution of tutorial 2
Preferably use double lap shear joints instead of single lap shear joint.
Enlarge the joint overlap area by increasing the number of rows and distance between each row.
Use staggered joints leading to smaller kb.

## Slide 57: Tutorial 3
Determine the load capacity of the L joint of next slide. Assume that sections are thin so effects of load eccentricity can be ignored. The plates have different thickness and 25 mm wide made of aluminium 2024-T3. The diameter of fastener is 4 mm. The shear off strength of fastener is 3620 N (2024-T31) - Consider ultimate loading scenario.
2024-T3 tensile strength = 483 MPa
2024-T3 yield strength = 345 MPa
2024-T3 shear strength = 283 MPa
2024-T3 yield bearing strength = 524 MPa
2024-T3 ultimate bearing strength = 855 MPa
2024-T3 Poisson’s ratio = 0.33
2024-T3 Young’s modulus of elasticity = 73.1 GPa
2024-T3 shear modulus of elasticity = 28 GPa

## Slide 58: Solution of tutorial 3
F
4 mm
4 mm
20 mm
The following failure types do not apply in this joint:
  Tension failure
  Bearing failure
  Tension cleavage
  Fastener shear-off
  Shear-out failure
The following failure types apply:
  Fastener pull-through
  Fastener tension failure
  Failure of joined sheets

## Slide 59: Solution of tutorial 3
Maximum possible force to avoid fastener tensile failure:
Check what force causes pull-through:
F
4 mm
4 mm
20 mm
P
15 mm

## Slide 60: Solution of tutorial 3
Check if the sheet itself fails due to prying effect:
F
4 mm
20 mm
P
15 mm
Ppr-eq
Ppr-eq
15 mm
13 mm
8.67 mm
4 mm
Sheet bending
If needed we can reduce conservatism and use 8.67 mm instead of e = 15 mm

## Slide 61: Solution of tutorial 3
Check if the flange of the sheet itself fails due to shear force:
F
4 mm
20 mm
P
15 mm
Ppr-eq

## Slide 62: Solution of tutorial 3
Check if the web of the sheet itself fails due to tensile loading:
4 mm
20 mm
P
15 mm
Ppr-eq
F

## Slide 63: Solution of tutorial 3
The final load capacity of the joint is the minimum of previous five calculated forces, i.e. 1209.23 N.