## Slide 1: Aero Structures-Shear of beams
By
Dr. Mahdi Damghani
2022-2023

## Slide 2: Suggested Readings
Chapter 16
of
Aircraft Structural Analysis
Notes: Questions here please:
https://padlet.com/mahdi_damghani/SDIAero

## Slide 3: Comments
https://padlet.com/damghani_mahdi/aerostructures

## Slide 4: Topics
Familiarisation with the following concepts;
  Shear of open section beams
  Shear centre of open section beams
  Shear of closed section beams
  Shear centre of closed section beams
  Twist of shear loaded closed section beams

## Slide 5: Overview

## Slide 6: Introduction
In this lecture we address thin-walled beams loaded in shear typical sections in the wing
Topics discussed here do not apply to thick and solid sections as they are not typical cross sections used in aircraft structures

## Slide 7: Why shear force in the wing section? (https://www.youtube.com/watch?v=YyeX6ArxCYI)
Notes: https://www.youtube.com/watch?v=YyeX6ArxCYI

## Slide 8: Why shear loading?
Centre spar
Front spar
Rear spar
Aerodynamic centre
For symmetric loading can be assumed clamped
Lift
Pitching moment

## Slide 9: Idealising wing as a cantilevered beam

## Slide 10: Stress system on element of a beam
We isolate this element of the beam as of the next slide
Direction of positive shears
Direction of positive shears

## Slide 11: Stress system on element of a beam
s is distance measured around the cross section from some convenient origin
An element of size is in equilibrium by a system of stresses
t is assumed to be constant along
shear flow which is positive in the direction of increasing

## Slide 12: Stress system on element of a beam
Equilibrium of forces in direction
Equilibrium of forces in sdirection

## Slide 13: Shear of open section beams
Shear forces Sx and Sy are applied at the point that does not create torsion in the section, i.e. shear centre
In the absence of hoop stresses (assumed)

## Slide 14: Shear of open section beams
If we take the origin of at the open edge of the cross section then when

## Slide 15: Shear of open section beams
For a section having either Cx or Cy as an axis of symmetry Ixy=0 and hence the relationship simplifies to;
0
0
0
0

## Slide 16: Example
Determine the shear flow distribution in the thin-walled Z-section shown in the figure due to a shear load applied through the shear centre of the section.

## Slide 17: Solution
Since the load is applied at shear centre that means no torsion takes place in the section
Therefore, shear stress and shear flow as the result of torsion does not exist
There is no axis of symmetry, hence we use the following equation for shear flow determination

## Slide 18: Solution
0
0

## Slide 19: Solution
Integration must be performed for the whole length of the cross section, i.e. path 12, 23 and 34

## Slide 20: Solution
20
Integration must be performed for the whole length of the cross section, i.e. path 12, 23 and 34
Obtained by in (shear flow at point 2)

## Slide 21: Solution
Positive q means that the shear flows in direction of s
You may use the following analogy to have a physical understanding of this phenomenon;
  Emptying a bucket of water at points of zero shear flow (brown spot) causes some of the water to go to the left and some to the right. Each path continues flowing until it gets drained, i.e. reach another zero point (red spot)

## Slide 22: Finite element simulation of previous example
Undeformed shape
Deformed shape
Shear flow

## Slide 23: Shear centre
Shear load applied at shear centre does not create torsion in the section
You could see the wooden support as fuselage and the channel beam as wing

## Slide 24: Shear centre
For cruciform or angle sections below, the shear centre lies at the intersection of the sides
Students are required to go through section 16.2.1 of Ref [1] (student centred activity) for obtaining the location of shear centre

## Slide 25: Example
Obtain shear flow distribution for a cantilevered beam with the C channel section with constant thickness . Assume the value of shear force acting on the section is . The section can be treated as thin wall section.
A
B
C
D
b
h

## Slide 26: Solution
h
The location of centroid from the mid line of BC;
A
B
C
D
b
h
x
y
d
h/2

## Slide 27: Solution
A
B
C
D
b
h
x
y
d
h/2

## Slide 28: Solution
A
B
C
D
b
h
x
y
d
h/2
s1
s2
s3

## Slide 29: Solution
A
B
C
D
b
h
x
y
d
h/2
s1
s2
s3

## Slide 30: Solution
A
B
C
D
b
h
x
y
d
h/2
s1
s2
s3

## Slide 31: Solution
Shear flow distribution becomes;
x
y

## Slide 32: Students’ task
Find the location of shear centre (distance e) for the C section of previous example.
A
B
b
x
y
d
h/2
s1
s2
s3
e
Sy

## Slide 33: Shear of closed section beams
Similar to open section beams with two differences:
  The shear loads may be applied through points in the cross section other than the shear centre so that torsional as well as shear effects are included;
  It is generally not possible to choose an origin for at which the value of shear flow is known.

## Slide 34: Shear of closed section beams
Just the same as open section beams
Unknown value of shear flow at origin (we choose where origin is)
Notes: Assuming there is no hoop stress and body forces

## Slide 35: Shear of closed section beams
Basic shear flow (that of an open section)
Unknown shear flow at an assumed origin
Shear flow of a closed section beam

## Slide 36: Shear of closed section beams
Now the question arises as how do we find the unknown shear flow at an assumed origin () and open section flow ()?
Convert the closed section to an open section
Equate torsion created by external shear force with that generated by internal shear flow
is obtained
𝑞_(𝑠,0) is obtained
Cut the section at a convenient point
At the cut and
At the cut 𝑠=0 and 𝑞=0
Obtain as you did for an open section
Obtain 𝑞_𝑏 as you did for an open section
Equate torsion created by external shear force with that generated by internal shear flow

## Slide 37: Shear of closed section beams
For open section we had;
Value of shear flow at the cut () can be found by;
We also know;
A is the area enclosed by midline of the beam section

## Slide 38: Shear of closed section beams
Note that if the moment centre chosen coincide with point of action of shear forces and then the equation can be simplified as;
0
0

## Slide 39: Twist of shear loaded closed section beams
If shear load is not applied to shear centre, twist of the section takes place
For detailed information of extracting the twist formula refer to section 16.3.1 of Ref [1]
The final twist equation is;
Rate of twist

## Slide 40: Example/Tutorial
Determine the shear flow distribution for a boxed beam under shear loading passing through the shear centre of the cross section.
Sy
t
a
b

## Slide 41: Solution
The shear load passes through the shear centre, so there is no torsion in the section;
The section is a closed section, hence we need to make it an open section first;
For this, we cut the section at an arbitrary point;
It is best to cut it at a point that passes through the neutral axis as normally shear flow is maximum at that point.
cut

## Slide 42: Solution
Let’s deal with basic shear flow first (open section shear flow);
cut
y
x

## Slide 43: Solution
y
x
1
2
3
4
5
6
s1
s2
Shear flow at the cut is zero

## Slide 44: Solution
y
x
1
2
3
4
5
6
s1
s2
s3
s4

## Slide 45: Solution
y
x
1
2
3
4
5
6
s1
s2
s3
s4
s5

## Slide 46: Solution
Now that we calculated basic shear flow we need to find
This is achieved by balancing internal moment and external moment about any point
For convenience we will take point as the point of action of shear load
By doing this the moment resulting from shear load disappears

## Slide 47: Solution
Sy
B
t
a
b
1
2
3
4
5
6
Since it is a thin wall section, I could ignore thickness effects. This will have negligible impact on the final solution.

## Slide 48: Solution
Sy
B
t
a
b
1
2
3
4
5
6
If ultimate precision was intended, I should have used .

## Slide 49: Solution
Sy
B
t
a
b
1
2
3
4
5
6

## Slide 50: Solution
Now the total shear flow will become (note that );
So far, we solved this problem parametically, i.e. in terms of section variables, and now this could be used for optimisation process

## Slide 51: Solution
I now embed this into excel that enables me to find shear flow for any box section of any dimension;
For illustration purposes I use the following values;

## Slide 52: Solution
qs,o is constant
Basic shear flow

## Slide 53: Solution
A tidier illustrative shear flow distribution is;
+
-
-
+
-
+
What does negative mean?

## Slide 54: Important note
Determination of shear flow distribution in multi-cellular section thin walled beams as stipulated in chapters 18 and 22 of Ref. [1] is fulfilled through successful implementation of student centered coursework released at the start of the semester;

## Slide 55: Tutorial 1

## Slide 56: Tutorial 2

## Slide 57: Tutorial 3