## Slide 1: Structural Design and Inspection-Principle of Virtual Work
By
Dr. Mahdi Damghani
2022-2023

## Slide 2: Suggested Readings
Reference 1
Reference 2
Notes: https://padlet.com/mahdi_damghani/SDIAero

## Slide 3: Objective(s)
Familiarity with the definition of work
Familiarity with the concept of virtual work by
  Axial forces
  Transverse shear forces
  Bending
  Torsion
Familiarisation with unit load method

## Slide 4: Introduction
They are based on the concept of work and are considered within the realm of “analytical mechanics”
Energy methods are fit for complex problems such as indeterminate structures
They are essential for using Finite Element Analysis (FEA)
They provide approximates solutions not exact
The Principle of Virtual Work (PVW) is the most fundamental tool of analytical mechanics

## Slide 5: Complexity Demonstration

## Slide 6: Work
Displacement of force times the quantity of force in the direction of displacement gives a scalar value called work

## Slide 7: Work on a particle
Point A is virtually displaced (imaginary small displacement) to point A’
R is the resultant of applied concurrent forces on point A
If particle is in equilibrium?
R=0
WF=0

## Slide 8: Principle of Virtual Work (PVW)
If a particle is in equilibrium under the action of several forces, the total work done by the forces for a small arbitrary displacement of the particle is zero. (Equivalent to Newton’s First Law)
Can we say?
If a particle is not in equilibrium under the action of a number of forces, the total work done by the forces for a small arbitrary displacement of the particle is not zero.
R could make a 90 degree angle with displacement

## Slide 9: In other words
The work done by a real force moving through an arbitrary virtual displacement ≈ arbitrary test displacement ≈ arbitrary fictitious displacement is called the virtual work . It is defined as;
Note that The word arbitrary is easily understood: it simply means that the displacements can be chosen in an arbitrary manner without any restriction imposed on their magnitudes or orientations. More difficult to understand are the words virtual, test, or fictitious. All three imply that these are not real, actual displacements. More importantly, these fictitious displacements do not affect the forces acting on the particle.
Then we define PVW for both rigid bodies and deformable bodies separately (see subsequent slides).

## Slide 10: Note 1
Note that, Δv is a small and purely imaginary displacement and is not related in any way to the possible displacement of the particle under the action of the forces, F;
Δv has been introduced purely as a device for setting up the work-equilibrium relationship;
The forces, F, therefore remain unchanged in magnitude and direction during this imaginary displacement;
This would not be the case if the displacements were real.

## Slide 11: PVW for rigid bodies
External forces (F1 ... Fr) induce internal forces;
Suppose the rigid body is given virtual displacement;
Internal and external forces do virtual work;
There are a lot of pairs like A1 and A2 whose internal forces would be equal and opposite;
We can regard the rigid body as one particle.
It does not undergo deformation (change in length, area or shape) under the action of forces.
Internal forces act and react within the system and external forces act on the system
Notes: The total virtual work done by all forces acting on a rigid body in static equilibrium is zero for small and admissible virtual displacements from the equilibrium state. In equation form it is written as above.

## Slide 12: PVW for deformable bodies
If a virtual displacement of Δ is applied, all particles do not necessarily displace to the amount of Δ, i.e. internal virtual work is done in the interior of the body.
This principle is valid for;
  Small displacements.
  Rigid structures that cannot deform.
  Elastic or plastic deformable structures.
  Competent in solving statically indeterminate structures.
The distance between two points changes under the action of forces.

## Slide 13: Work of internal axial force on mechanical systems/structures
Isolate
Section
This truss element is working under the action of axial load only as a result of external aerodynamic loading.
After imposing a virtual displacement, the axial load does virtual work on this truss element.
To obtain the amount of virtual work, we obtain the work on the section and then throughout the length (next slide).
Arbitrary section shape

## Slide 14: Work of internal axial force
Work done by small axial force due to small virtual axial strain for an element of a member:
Work done by small axial force due to small virtual axial strain for a member:
Work done by small axial force due to small virtual axial strain for a structure having r members:
δN=N/A δA

## Slide 15: Work of internal axial force for linearly elastic material
Based on Hook’s law (subscript v denotes virtual);
Therefore, we have (subscript m denotes member m);

## Slide 16: Work of internal shear force
Work done by small shear force due to small virtual shear strain for an element of a member (β is form factor):
Work done by small shear force due to small virtual shear strain for a member of length L:
δS
Work done by small shear force due to small virtual shear strain for a structure having r members:

## Slide 17: Work of internal shear force for linearly elastic material
Based on Hook’s law (subscript v denotes virtual);
Therefore, we have (subscript m denotes member m);

## Slide 18: Work of internal bending moment
Work done by small bending due to small virtual axial strain for an element of a member:
Work done by small bending due to small virtual axial strain for a member:
Work done by small bending due to small virtual axial strain for a structure having r members:
Radius of curvature due to virtual displacement

## Slide 19: Work of internal bending moment for linearly elastic material
We have (subscript m denotes member m);

## Slide 20: Work of internal torsion
See chapter 2 of Reference 1, chapter 15 of Reference 2 or chapter 9 of Reference 3 for details of this
Following similar approach as previous slides for a member of length L we have;
For a structure having several members of various length we have;

## Slide 21: Virtual work due to external force system
If you have various forces acting on your structure at the same time;

## Slide 22: Note
So far virtual work has been produced by actual forces in equilibrium moving through imposed virtual displacements;
Based on PVW, we can alternatively assume a set of virtual forces in equilibrium moving through actual displacements;
Application of this principle, gives a very powerful method to analyze indeterminate structures;

## Slide 23: Example 1
Determine the bending moment at point B in the simply supported beam ABC.

## Slide 24: Solution
We must impose a small virtual displacement which will relate the internal moment at B to the applied load;
Assumed displacement should be in a way to exclude unknown external forces such as the support reactions, and unknown internal force systems such as the bending moment distribution along the length of the beam.

## Slide 25: Solution
Using conventional equations of equilibrium method;
RA
RC

## Slide 26: Solution
Let’s give point B a virtual displacement;
β
Rigid
Rigid

## Slide 27: Example 2
Using the principle of virtual work, derive a formula in terms of a, b, and W for the magnitude P of the force required for equilibrium of the structure below, i.e. ABC (you may disregard the effects of weight).
W
P

## Slide 28: Solution
We assume that AB and AC are rigid and therefore internal work done by them is zero
Apply a very small virtual displacement to our system
Just to confirm the answer, you would get the same result if you took moment about B, i.e.
W
P

## Slide 29: Example 3
Calculate the force in member AB of truss structure?

## Slide 30: Solution
This structure has 1 degree of indeterminacy, i.e. 4 reaction (support) forces, unknowns, and 3 equations of equilibrium
Let’s apply an infinitesimally small virtual displacement where we intend to get the force
Equating work done by external force to that of internal force gives

## Slide 31: Example 4
We would like to obtain slope for the portal frame below;
P

## Slide 32: Solution
P

## Slide 33: Note
The amount of virtual displacement can be any arbitrary value;
For convenience lets give it a unit value. For example, in the previous example lets say Δv,B=1;
In this case the method could be called unit load method.

## Slide 34: Note
If you need to obtain force in a member, you should apply a virtual displacement at the location where force is intended;
If you need to obtain displacement in a member, you should apply a virtual force at the location displacement is intended.

## Slide 35: Example 5
Determine vertical deflection at point B using unit load method.

## Slide 36: Solution
Apply a virtual unit load in the direction of displacement to be calculated
Work done by virtual unit load
Work done by internal loads
Equating external work with internal
Virtual system
Real system

## Slide 37: Example 6
Using unit load method determine slope and deflection at point B.
A
C
B
D
5kN/m
IAB=4x106 mm4
IBC=8x106 mm4
8kN
2m
0.5m
0.5m
E=200 kN/mm2

## Slide 38: Solution
For deflection we apply a unit virtual load at point B in the direction of the intended displacement;
Virtual system
Real system
Segment | Interval | I (mm4) | M v (kN.m) | M (kN.m)
AD | 0<x<0.5 | 4x106 | 0 | 8x
DB | 0.5<x<1 | 4x106 | 0 | 8x-2.5(x-0.5)2
BC | 1<x<3 | 8x106 | -x+1 | 8x-2.5(x-0.5)2

## Slide 39: Solution
For slope we apply a unit virtual moment at point B
1kN.m

## Slide 40: Solution
Segment | Interval | I (mm4) | M v (kN.m) | M (kN.m)
AD | 0<x<0.5 | 4x106 | 0 | 8x
DB | 0.5<x<1 | 4x106 | 0 | 8x-2.5(x-0.5)2
BC | 1<x<3 | 8x106 | 1 | 8x-2.5(x-0.5)2

## Slide 41: Q1
Use the principle of virtual work to determine the support reactions in the beam ABCD.

## Slide 42: Q2
Find the support reactions in the beam ABC using the principle of virtual work.

## Slide 43: Q3
Find the bending moment at the three-quarter-span point in the beam. Use the principle of virtual work.

## Slide 44: Q4
Use the unit load method to calculate the deflection at the free end of the cantilever beam ABC.

## Slide 45: Q5
Calculate the deflection of the free end C of the cantilever beam ABC using the unit load method.

## Slide 46: Q6
Use the unit load method to find the magnitude and direction of the deflection of the joint C in the truss. All members have a cross-sectional area of 500mm2 and a Young’s modulus of 200,000 N/mm2.

## Slide 47: Q7
Calculate the forces in the members FG, GD, and CD of the truss using the principle of virtual work. All horizontal and vertical members are 1m long.